## Slide 1
MOS Gates

## Slide 2: Terminal Voltages
Mode of operation depends on Vg, Vd, Vs
  Vgs = Vg – Vs
  Vgd = Vg – Vd
  Vds = Vd – Vs = Vgs - Vgd
Source and drain are symmetric diffusion terminals
  By convention, source is terminal at lower voltage
  Hence Vds  0
nMOS body is grounded. First assume source is 0 too.
Three regions of operation
  Cutoff
  Linear
  Saturation

## Slide 3: nMOS Cutoff
No channel
Ids ≈ 0

## Slide 4: nMOS Linear
Channel forms
Current flows from d to s
  e- from s to d
Ids increases with Vds
Similar to linear resistor

## Slide 5: nMOS Saturation
Channel pinches off
Ids independent of Vds
We say current saturates
Similar to current source

## Slide 6: I-V Characteristics
In Linear region, Ids depends on
  How much charge is in the channel?
  How fast is the charge moving?
Ids is dependent on both Vds and Vgs

## Slide 7
Transfer characteristics (n channel FET)
Operating range decides the type of FET
G
S
D

## Slide 8
NMOS Inverter
Inverter Operation
- Plus signal input turns transistor on
- Ground is connected to output, thus a 1 (+) in gives 0 (Gnd) out
- A 0 input opens transistor and output is pulled high by resistor
Enhancement NMOS: (a) ID versus VDS (b) ID versus VGS

## Slide 9
NMOS Inverter
Resistor dissipates heat
Fabrication of resistor is not easy
Even modest values of Resistors occupy excessively large areas in silicon substrate

## Slide 10
A transistor may be used as a resistor
VDD
Input
Output
Pull up
Pull down
In Pull down NMOS
For input=1, Pull down conducts
For input =0, Pull down is off

## Slide 11
Pull up as an enhancement type NMOS
VDD
Input
Output
Pull up
Pull down
Pull up transistor input (VGG) should be high
VGG

## Slide 12
Pull up as an enhancement NMOS
VDD
Input
Output
Pull up
Pull down
Dissipation is high since current flows when input=1
Vout can never be zero
Vout can never reach VDD (logical 1) if VGG=VDD as is normally the case
If VGG is higher than VDD, then an extra rail is required
VGG
VDD
Vout
Vin
Vtpd
Vtpu
Non zero output

## Slide 13
VDD
Input
Output
Depletion type NMOS is used in pull up for better performance
Gate and Source is shorted to achieve VGS=0
In Pull down NMOS
For input=1, Pull down is on
For input =0, Pull down is off
Pull up is always on

## Slide 14
VDD
Input
Output
Depletion type NMOS is used in pull up for better performance
VDD
Vout
Vin
Vtpd
Non zero output
Current flows
No current
Dissipation is high since current flows when input=1
Vout can never be zero

## Slide 15: Drawbacks of Metal-gate MOS Transistors
High current flow for input at logic 1 in case of an inverter
Excess surface state charges and mobile ion contamination cause the threshold variation.
Vout never becomes exactly zero
Suffer from excessive overlap capacitance.
Parasitic capacitances Cgs and Cgd slow the transistor because they must be charged and discharged during switching.
Aluminum is used as gate material which can erode completely causing contact spiking.

## Slide 16: Complementary MOS Transistors (CMOS)
p
n
GND
VDD
A
Y = A'
When A is pulled high (VDD), the PMOS inverter is turned off, while the NMOS is turned on pulling the output down to VSS
When A is pulled low (VSS), the NMOS inverter is turned off, while the PMOS is turned on pulling the output up to VDD

## Slide 17: Complementary MOS Transistors (CMOS)
p
n
GND
VDD
A
Y = A'
VDD
Vout
Vin
Vtpd
Both on
n on
p off
p on
n off
No current flow either for logical 0 or for logical 1 inputs
Full logical 1 and 0 levels are presented at output
For devices of similar dimension p-channel is slower than n-channel device

## Slide 18: Complementary MOS Transistors (CMOS)
p
n
GND
VDD
A
Y = A'
D
D
S
S
G
G

## Slide 19: Types of MOSFET
Pullup may be enhancement type PMOS

## Slide 20: CMOS Inverter Technology
Complementary MOS, or CMOS, needs both PMOS and NMOS devices for their logic gates to be realized
The concept of CMOS was introduced in 1963 by Wanlass and Sah, but it did not become common until the 1980’s as NMOS microprocessors were dissipating as much as 50 W and alternative design technique was needed
CMOS still dominates digital IC design today

## Slide 21: CMOS Inverter
Circuit schematic for a CMOS inverter
Simplified operation model with a high input applied
Simplified operation model with a low input applied

## Slide 22
Speed / power performance of available technologies