## Slide 1
Localization of mobile devices
Nandini Mukherjee
Dept. of Computer Science and Engineering, Jadavpur University

## Slide 2
Localization
A node needs to determine its physical position (with respect to some coordinate system) or symbolic location
Required since many applications such as environment monitoring, vehicle tracking and mapping depend on knowing the locations of sensor nodes
location-based routing protocols can also
  save significant energy by eliminating the need for route discovery
  improve caching behavior for applications where requests may be location dependent
  enhance security by location awareness (for example, preventing wormhole attacks

## Slide 3
Localization Problem
Problems:
  the network can consist of a large number of nodes that are deployed in an ad-hoc fashion, the exact node locations are not known a-priori
  One straightforward solution is to add GPS to all the nodes in the network
  But the above solution is not practical since:
    GPS cannot work indoors or in the presence of dense vegetation, foliage or other obstacles that block the line-of-sight from the GPS satellites.
    The power consumption of GPS will reduce the battery life on the sensor nodes thus reducing the effective lifetime of the entire network.
    The production cost factor of GPS can become an issue when large numbers of nodes are to be produced.
    The size of GPS and its antenna increases the sensor node form factor. Sensor nodes are required to be small and unobtrusive.

## Slide 4
Localization
Major techniques depend on
  Using the help of anchor nodes that know the positions of other nodes
  Directly adjacent or over multiple hops
  Using different means to determine distances/angles locally

## Slide 5
Localization & positioning
Determine physical position or logical location
  i.e. coordinate system or symbolic reference
  In other words, absolute or relative coordinates
Options
  Either centralized or distributed computation
  May scale for indoors, outdoors or global
  There may be different sources of information
Metrics
  Accuracy (how close is an estimated position to the real position?)
  Precision (for repeated position determinations, how often is a given accuracy achieved?)
  Costs, energy consumption etc.

## Slide 6
Localization - approaches
Majority of existing location discovery approaches consist of two basic phases:
  (1) distance (or angle) estimation
  (2) distance (or angle) combining
Distance between two nodes may be estimated by using:
  Received Signal Strength Indicator (RSSI)
    measure the power of the signal at the receiver based on the known transmit power, the effective propagation loss can be calculated
      Send out signal of known strength, use received signal strength and path loss coefficient to estimate distance
    theoretical and empirical models are used to translate this loss into a distance estimate
    this method has been used mainly for RF signals.
    Problem: Highly error-prone process

## Slide 7
Localization - approaches
  Time based methods (ToA,TDoA)
    Record the time-of-arrival (ToA) or time-difference-of-arrival (TDoA). The propagation time can be directly translated into distance, based on the known signal propagation speed. These methods can be applied to many different signals, such as RF, acoustic, infrared and ultrasound.
    ToA
      Use time of transmission, propagation speed, time of arrival to compute distance
      Problem: Exact time synchronization
    TDoA
      Use two different signals with different propagation speeds
      Example: ultrasound and radio signal
        Propagation time of radio negligible compared to ultrasound
      Compute difference between arrival times to compute distance
      Problem: Calibration, expensive/energy-intensive hardware

## Slide 8
One-way ToA
  one-way propagation of signal
  requires highly accurate synchronization of sender and receiver clocks
    Dist(i,j) = (t2 − t1) *v
Two-way ToA
  round-trip time of signal is measured at sender device
  third message if receiver wants to know the distance
    Dist(i,j) = (((t4 − t1) − (t3 − t2 )) / 2) * v

## Slide 9
Time Difference of Arrival (TDoA)
  radio signal (sent at t1 and received at t2), followed by ultrasound signal
    (sent at t3=t1+twait and received at t4)
    dist = (v1 − v2) *(t4 − t2 − twait)
  no clock synchronization required
  distance measurements can be very accurate
  need for additional hardware

## Slide 10
Localization - approaches
  Angle -of -Arrival (AoA)
    estimate the angle at which signals are received and use simple geometric relationships to calculate node positions.

## Slide 11
Localization - approaches
For the combining phase, the most popular alternatives are:
  The most basic and intuitive method is called hyperbolic trilateration. It locates a node by calculating the intersection of 3 circles.
  Triangulation is used when the direction of the node instead of the distance is estimated, as in AoA systems. The node positions are calculated using the trigonometry laws of sines and cosines.
  The third method is Maximum Likelihood (ML) estimation. It estimates the position of a node by minimizing the differences between the measured distances and estimated distances.

## Slide 12
Hyperbolic trilateration
Triangulation
Maximum Likelihood

## Slide 13: Trilateration
n anchor nodes: xi=(xi,yi) (i=1..n)
Unknown sensor location x=(x,y)
Distances between sensor and anchors known (ri, i=1..n)
can be represented as Ax=b, such that A and b are as follows:

## Slide 15
Multilateration
Atomic Multilateration
  Requirement 1
    Atomic multilateration can take place if the unknown node is within one hop distance from at least three beacon nodes. The node may also estimate the ultrasound propagation speed if four or more beacons are available.
    It is a requirement, but not always sufficient. e.g. when beacons are in straight line

## Slide 16: Multilateration
Iterative Multilateration
    The unknown node becomes a beacons after its position is estimated
    Drawback – the error will be accumulated

## Slide 18
Iterative multilateration – Error accumulates

## Slide 19: Multilateration
Collaborative Multilateration
  goal: construct a graph of participating nodes, i.e., nodes that are anchors or have at least three participating neighbors
  node then tries to estimate its position by solving the corresponding system of simultaneous quadratic equations relating the distances among the node and its neighbors

## Slide 20: A good and a bad case of collaborative multilateration
Location of nodes 2 and 4 can be estimated in Figure 1
2 possible locations for node 4 in Figure 2

## Slide 21
Multihop range estimation
How to estimate range to a node to which no direct radio communication exists?
  No RSSI, TDoA
  But: Multihop communication is possible
Idea 1: Count number of hops, assume length of one hop is known (DV-Hop)
  Start by counting hops between anchors, divide known distance
Idea 2: If range estimates between neighbors exist, use them to improve total length of route estimation in previous method (DV-Distance)

## Slide 22
DV-Hop propagation method
The most basic scheme
It employs a classical distance vector exchange so that all nodes in the network get distances, in hops, to the landmarks
Each node maintains a table (Xi , Yi, hi) and exchanges updates only with its neighbors
Once a landmark gets distances to other landmarks, it estimates an average size for one hop, which is then deployed as a correction to the entire network
When receiving the correction, an arbitrary node may then have estimated distances to landmarks, in meters, which can be used to perform the triangulation
The correction a landmark (Xi; Yi) computes is

## Slide 23
DV-Hop propagation method
Three landmarks compute corrections which are actually average size of each hop.
A regular node gets an update from one of the landmarks (usually the closest one)
Corrections are distributed by controlled flooding, meaning that once a node gets and forwards a correction, it will drop all the subsequent ones
This policy ensures that most nodes will receive only one correction, from the closest landmark

## Slide 24
DV-Hop propagation method
Controlled flooding helps keeping the corrections localized in the neighborhood of the landmarks they were generated from.
When A gets its correction from L2, its estimated distances to the three landmarks would be:
  to L1: 3 x 16:42,
  to L2; 2 x 16:42,
  to L3; 3 x 16:42.
These values are then plugged into the triangulation procedure to get an estimated location for A
The technique is simple and it does not depend on measurement error
However, the algorithm works for the networks, when the properties of the graph are same in all directions
Thus the corrections that are deployed reasonably estimate the distances between hops

## Slide 25
DV-distance propagation method
This method is similar with the previous one with the difference that distance between neighboring nodes is measured using radio signal strength and is propagated in meters rather than in hops
As a metric, the distance vector algorithm is now using the cumulative traveling distance, in meters
On one hand the method is less coarse than “DV-hop”, because not all hops have the same size
On the other hand it is sensitive to measurement errors.

## Slide 26
Euclidean propagation method
The third scheme works by propagating the true euclidean distance to the landmark
An arbitrary node A needs to have at least two neighbors B and C which have estimates for the landmark L
Measured estimates of distances for AB, AC, and BC are also available
  there is the condition that: B and C, besides being neighbors of A, are neighbors of each other
Thus, for the quadrilateral ABCL, all the sides are known, and one of the diagonals, BC is also known
This allows node A to compute the second diagonal AL, which in fact is the euclidean distance from A to the landmark L
A may be on the same side of BC as L in which case the distance to L is different
The choice between the two possibilities is made locally by A either by voting, when A has several pairs of immediate neighbors with estimates for L, or by examining relation with other common neighbors of B and C

## Slide 27
Euclidean propagation method

## Slide 28
Localisation for a general network environment
Problems with earlier methods are:
  Dependence on special hardware
    Measuring ranging information from signal strength, time of arrival, time difference of arrival or angle of arrival require special hardware
    Adding the required hardware increases the cost and size of the nodes
  Requirement for particular network topologies
    Prior deployment of seeds (anchors) is not possible in many sensor network applications
    Hop count based techniques avoid the need for a large number of seeds, but instead require dense and uniform node distribution

## Slide 29
Localisation for a general network environment
Hu and Evans proposes algorithm for network where
  no special hardware for ranging is available
  the prior deployment of seed nodes is unknown
  the seed density is low, the node distribution is irregular
  nodes and seeds can move uncontrollably
  mobility of nodes is used to increase accuracy
Three kinds of scenarios
  Nodes are static, seeds are moving
  Nodes are moving, seeds are static
  Both nodes and seeds are moving

## Slide 30
Localisation for a general network environment
Since a node may move away from its previous location, it needs to re-localize in each time unit.
As a node moves in the network, prior location information becomes increasingly inaccurate.
On the other hand, there are new observations from seed nodes that are able to filter impossible locations.
Posterior distribution of a node’s possible locations after movement and observation is based on a simulation-based method called “Sequential Monte Carlo”

## Slide 31
Location Estimation Algorithm
Initialization: Initially the node has no knowledge of its location. N is a constant that denotes the number of samples to maintain
L0 = { set of N random locations in the deployment area }
Step: Compute a new possible location set Lt based on Lt-1, the possible location set from the previous time step, and the new observations, ot
Lt = { }
while (size (Lt) < N) do
R = {lti | lti is selected from p(lti | lt-1i) , lt-1i  Lt-1 for all 1 <= i <= N } //Prediction
Rfiltered = {lti | lti , where lti  R and p(lti | ot ) > 0 } //Filtering
Lt = choose (Lt Rfiltered , N)

## Slide 32
Location Estimation Algorithm
p(lti | lt-1i) describes the prediction of node’s current position based on previous position
p(lti | ot ) describes the likelihood of the node being at the location lt given the observations
A set of N samples Lt is used to represent the distribution lt
The algorithm recursively computes the set of samples at each time step
lt can be computed using only Lt-1 and ot

## Slide 33
Location Estimation Algorithm
Initially, it is assumed that the node has no knowledge about its position
Initial samples are selected randomly from all possible locations
At each time step, the location set is updated based on possible movements and new observations
Location of the node is computed by computing the average location of all possible locations in Lt

## Slide 34
Prediction
From the set of possible locations computed in the previous step, Lt-1, a set of new samples, Lt ,is obtained by applying the mobility model to each sample
A node may be unaware of its moving speed and direction, other than knowing its speed is less than vmax
So, if in previous step lt-1i is one possible position of a node, the possible current positions are contained in the circular region with origin lt-1i and radius vmax
Hence, the set R computed in the prediction phase contains one location selected randomly from the circle of radius vmax around every point in Lt-1

## Slide 35
Prediction
This reflects the increased uncertainty about the node’s location because of unknown motion
In cases where something is known about the node’s motion (for example, that it is moving at a particular speed, or that it is more likely to be moving in a certain direction), the probability distribution can be adjusted accordingly to make better predictions.

## Slide 36
Filtering
In this step, the node filters the impossible locations based on new observations
At time t, every node within radio range of a seed will hear a location announcement from that seed
  In a realistic deployment, it would be necessary to deal with network collisions and account for missed messages
There are four types of seeds to consider:
  outsiders – seeds that were not heard in either the current or the previous time quanta
  arrivers – seeds that were heard in the current time quantum, but not in the previous one
  leavers – seeds were heard in the previous time quantum, but not in this one
  insiders – seeds that were heard in both time quanta

## Slide 37
Filtering
Two approaches may be followed to gather this information:
  A seed node (S) transmits both its current location and its location at the previous time step in each announcement:
S  Region HELLO | IDS | loct | loct-1
  Neighbor nodes can transmit information about seed locations (the set of all seeds and their locations heard in the previous time step):
S  Region HELLO | IDS | loct
N  Region HELLO | IDN | {( IDS, locSt) }

## Slide 38
Filtering
Using the second approach a node can discover information about the insider and outsider of a seed.
Let S denotes the set of all seeds heard by N and T denotes the set of all nodes heard by N’s neighbors but not by N.
Then the filter condition of location l is
filter(l) = s  S, d(l, s)  r  s  T, r < d(l, s)  2r
p(lti | ot ) is zero if the filter condition is false
Locations that are inconsistent with observations are eliminated in this way from the possible location set
After filtering, there may be fewer than N possible locations remaining
The prediction and filtering processes repeat, unioning the possible points found, until at least N possible locations have been acquired
Choice of N affects accuracy